## Slide 1: Sensor Fusion Toolbox for Rocket Motion
Luke Aagaard, Kian Jamal, Nathan Tardy, 4/11/2024

## Slide 2: Data Generation
Simulink model
  1-D lookup table outputs Aerotech G25W Thrust curve using simulation time (thrust curve data taken from thrustcurve.org).
  Three-axis Inertial Measurement Unit data simulation outputs simulated noisy accelerometer and gyroscope data
  3DOF block applies the equations of motion (EOM)
04/10/2024
Luke Aagaard
2
1-D lookup table.
3DOF EOM block.
Three-axis IMU simulation block.

## Slide 3: Data Generation
Simulink model
MATLAB
% Luke Aagaard
% AEE 3150 Team Project
% March 28, 2024
clc; clear; close all; format compact;
Simulation_Time = 13; %s
sim('RocketLander_version3.mdl',Simulation_Time)
AccelerationData = load('IMU_noisy_data.mat')
AccelerationData = struct2array(AccelerationData)
AccelerationData = AccelerationData';
04/10/2024
Luke Aagaard
3
3DoF animation block graphic

## Slide 4: Data Processing
Input: raw (noisy) data from virtual sensors
4/9/2024
Nathan Tardy
4
Linear acceleration along body axes
Angular velocity along body axes
Only really 1 non-zero component due to nature of the motion
No yaw
No roll

## Slide 5: Data Processing
4/9/2024
Nathan Tardy
5
Method: FFT on noisy data (HW 4)

## Slide 6: Data Processing
4/9/2024
Nathan Tardy
6
Thin lines: noisy signal
Thick lines: cleaned signal (n = 11)